## Slide 1: Water Pollution
Dr. Sireen Alkhaldi/ Community Medicine

## Slide 2: Water Situation
85% of the world population lives in the driest half of the planet (United Nations, 2013)
1 billion people do not have access to clean water and almost 2.5 billion do not have access to adequate sanitation.
2 million people die each year due to unsafe water, sanitation and hygiene (WHO, 2015).

## Slide 3
The Hydrologic cycle
( the water cycle)

## Slide 4: World Freshwater Supply

## Slide 5: Water Pollution
According to the definition of the World Health Organisation (WHO) (1966), water pollution occurs when:
“foreign materials either from natural or other sources are contaminated with water supplies and may be harmful to life, because of their toxicity, reduction of normal oxygen level of water, aesthetically unsuitable effects and spread of epidemic diseases”.

## Slide 6: Two Sources of Water Pollution
Although water pollution occurs from a variety of sources, there are two terms used to describe how the water becomes polluted:
1. Point sources
2. Non-point sources

## Slide 7
Point Source Pollution
1. comes from a specific source, like a pipe. Pollution will be located at a specific place.
2. Sources are: factories, industry, municipal treatment plants
3. Easy to identify, monitor and regulate.
The BP oil spill in 2010 is an example of point source pollution, because the massive amount of oil leaked from a single point of origin.

## Slide 8: Point and Nonpoint Sources
NONPOINT SOURCES
Urban streets
Suburban development
Wastewater treatment plant
Rural homes
Cropland
Factory
Animal feedlot
POINT SOURCES
Fig. 22-4 p. 494

## Slide 9
What is nonpoint source pollution?
Nonpoint Source (NPS) Pollution is pollution associated with storm water or runoff.
Difficult to identify and control
Broad and Diffuse area is affected
Expensive to clean up.
For example, one water body (river or sea) may be contaminated by multiple sources like agricultural runoff, city street runoff, construction sites and residential lawns (e.g. The Mississippi River).

## Slide 10: Nonpoint Sources
Agriculture activities: a leading cause of water pollution:
  Sediment eroded from the lands
  Fertilizers and pesticides
  Bacteria from livestock and food processing wastes
Industrial facilities
Mining
Transportation, roads and parking lots
Human-made materials (E.g., plastics)

## Slide 11
Examples of NPS
oil & grease from cars
fertilizers
animal waste
grass clippings
septic systems
sewage
household cleaning products
litter

## Slide 13
Pollutant Transport Mechanisms
NPS pollutants build up on land surfaces during dry weather
  Atmospheric deposition
  Fertilizer applications
  Animal waste
  Automotive exhaust/fluid leaks
Pollutants are washed off land surfaces during precipitation events (stormwater runoff)
Stormwater runoff will flow to lakes and streams

## Slide 14: Point Source of Polluted Water in Gargas, France

## Slide 15: Nonpoint Sediment from Unprotected Farmland Flows into Streams

## Slide 16
Linking Land Use to Water Quality
More Imperviousness = More Polluted Water

## Slide 17
What is impervious cover?
Impervious cover is: roads, rooftops, parking lots, and other hard surfaces that do not allow stormwater to soak into the ground.
provides a surface for accumulation of pollutants
leads to increased polluted runoff and flooding
inhibits recharge of groundwater

## Slide 18
Potential Sources of Pollutants Found in Residential Areas
Nutrients: Fertilizers and septic systems (sewage)
Pathogens: Pet waste and septic systems (sewage)
Sediment: Construction, road sand, soil erosion
Toxic: Pesticides, household products
Debris: Litter and illegal dumping
Thermal: heated runoff

## Slide 19
Pollutants Found in Runoff
Sediment
  Soil particles transported from their source
Biochemical Oxygen Demand (BOD)
● Oxygen depleting material
  Leaves
  Organic material
Toxics
  ● Pesticides
    Herbicides
    Fungicides
    Insecticides
  ● Metals (naturally occurring in soil, automotive emissions/ tires)
    Lead
    Zinc
    Mercury
  ● Petroleum Hydrocarbons (automotive exhaust and fuel/oil)
Debris
  Litter and illegal dumping
Nutrients
  ● Various types of materials that become dissolved and suspended in water (commonly found in fertilizer and plant material):
    Nitrogen (N)
    Phosphorus (P)
Bacteria/ Pathogens
Originating from:
  ● Pets
  ● Waterfowl
  ● Failing septic systems
Thermal Stress
  Heated runoff, removal of streamside vegetation

## Slide 20: Storm Sewer and Sanitary Sewage System

## Slide 21: Natural Capital Degradation: Highly Polluted River in China

## Slide 22: Trash Truck Disposing of Garbage into a River in Peru

## Slide 23: India’s Ganges River

## Slide 24: What Are the Major Water Pollution Problems in Streams and Lakes?
While streams are extensively polluted worldwide by human activities, they can cleanse themselves of many pollutants if we do not overload them or reduce their flows.
Addition of excessive nutrients to lakes from human activities can disrupt lake ecosystems, and prevention of such pollution is more effective and less costly than cleaning it up.
Biodegradation of wastes by bacteria takes time.

## Slide 25: Natural Purification Processes

## Slide 26: Eutrophication
“The enrichment of bodies of fresh water by nutrients (e.g. nitrate, phosphate). These typically promote excessive growth of algae.
Eutrophication is a natural, slow-aging process for a water body, but human activity greatly speeds up the process (e.g. fertilizer runoff and sewage discharge) and is particularly evident in slow-moving rivers and shallow lakes.

## Slide 27: Pollution of Lakes (eutrophication)
Eutrophication
Fig. 22-7 p. 499

## Slide 28: Pollution Problems Affecting Groundwater
Ground water is a source of drinking water
Chemicals used in agriculture, industry, transportation, and homes can spill and leak into groundwater and make it undrinkable.
There are simple ways and complex ways to purify drinking water, but protecting it through pollution prevention is the least expensive and most effective strategy.

## Slide 29: Ground Water Cannot Cleanse Itself Very Well
Common pollutants of ground water are:
  Fertilizers and pesticides, Gasoline, and Organic solvents
Pollutants are dispersed in a wide area.
Slower chemical reactions in groundwater due to
  Slow flow: contaminants not diluted
  Less dissolved oxygen
  Fewer decomposing bacteria

## Slide 30
Fig. 20-11, p. 542
Polluted air
Hazardous waste injection well
Pesticides and fertilizers
Deicing road salt
Coal strip mine runoff
Buried gasoline and solvent tanks
Pumping well
Gasoline station
Cesspool, septic tank
Waste lagoon
Sewer
Water pumping well
Landfill
Leakage from faulty casing
Accidental spills
Discharge
Groundwater flow
Unconfined freshwater aquifer
Confined freshwater aquifer
Confined aquifer
Notes: Figure 20.11
Natural capital degradation: principal sources of groundwater contamination in the United States (Concept 20-3A). Another source is saltwater intrusion from excessive groundwater withdrawal in coastal areas. (Figure is not drawn to scale.) Question: What are three sources shown in this picture that might be affecting groundwater in your area?

## Slide 31
Fig. 20-12, p. 543
Leaking tank
Aquifer
Bedrock
Water table
Groundwater flow
Gasoline leakage plume (liquid phase)
Free gasoline dissolves in groundwater (dissolved phase)
Migrating vapor phase
Contaminant plume moves with the groundwater
Water well
Notes: Figure 20.12
Natural capital degradation: groundwater contamination from a leaking gasoline tank. As the contaminated water spreads from its source in a widening plume, it can be extracted by wells used to provide water for drinking and irrigation.

## Slide 32: Pollution Problems Affecting Sea water and Oceans
The great majority of ocean pollution originates on land and includes oil, sewage, agricultural runoff, and other toxic chemicals and solid wastes, which threaten aquatic species and other wildlife and disrupt marine ecosystems.
The key to protecting the oceans is to reduce the flow of pollutants from land and air and from streams emptying into these waters.

## Slide 33
Fig. 20-15, p. 548
Industry Nitrogen oxides from autos and smokestacks, toxic chemicals, and heavy metals in effluents flow into bays and estuaries.
Cities Toxic metals and oil from streets and parking lots pollute waters; sewage adds nitrogen and phosphorus.
Urban sprawl
Bacteria and viruses from sewers and septic tanks contaminate shellfish beds and close beaches; runoff of fertilizer from lawns adds nitrogen and phosphorus.
Construction sites
Sediments are washed into waterways, choking fish and plants, clouding waters, and blocking sunlight.
Farms
Runoff of pesticides, manure, and fertilizers adds toxins and excess nitrogen and phosphorus.
Red tides
Excess nitrogen causes explosive growth of toxic microscopic algae, poisoning fish and marine mammals.
Toxic sediments
Chemicals and toxic metals contaminate shellfish beds, kill spawning fish, and accumulate in the tissues of bottom feeders.
Oxygen-depleted zone Sedimentation and algae overgrowth reduce sunlight, kill beneficial sea grasses, use up oxygen, and degrade habitat.
Healthy zone
Clear, oxygen-rich waters promote growth of plankton and sea grasses, and support fish.
Closed shellfish beds
Closed beach
Oxygen-depleted zone
Notes: Figure 20.15
Natural capital degradation: residential areas, factories, and farms all contribute to the pollution of coastal waters and bays. According to the U.N. Environment Programme, coastal water pollution costs the world $16 billion annually—more than $30,000 a minute—due to ill health and premature death. Question: What are three changes you could make in your lifestyle that might help to prevent this pollution?

## Slide 34: Ocean Oil Pollution Is a Serious Problem
Crude and refined petroleum are highly disruptive pollutants
Largest source of ocean oil pollution is urban and industrial runoff from land
Volatile organic hydrocarbons (Kill many aquatic organisms)
Tar-like globs on the ocean’s surface (Coat animals)
Heavy oil components sink (Affect the bottom dwellers)
Faster recovery from crude oil than refined oil
Methods of preventing oil spills should be strictly used.

## Slide 35: Controlling Water Pollution:
There should be vigorous efforts to control water pollution with the involvement of individuals, communities, governments and social activist groups.
Mass social awareness should be inculcated regarding the nature and effects of water pollution, and remedial measures.
Strict laws should be enforced, and persons violating the provision of pollution control should be penalized.

## Slide 36
Water use in Jordan